## Slide 1: A History of LD for Optical Communication in NTT -Platform of INTERNET Society-
Larry Coldren Symposium, 16 March ‘18
Tetsu IKEGAMI
Advisor NTT etc.
President of LEOS in 1994
President, NTT Labs, 1996
tetsu-ikegami@poplar.ocn.ne.jp
Access to: britta@engineering.ucsb.edu
DFB LD Δf 80 kHz
1971
2018

## Slide 2: What we learn from OFC ‘18
Frequency
Efficiency
Spectrum
Space
(Distance, NWing)
M. Weldon, Nokia Bell Labs, USA
Chengliang Zhang, China Telecom
Beijing Research Institute
”Optical NWing in the Cloud
and 5G Era”
工欲善其“事” 必先利其“器”
by 孔子 (Confucius)
To accomplish the MISSION, one must sharpen his TOOLs
”The Future of Deterministic
Dynamic Networking”
Low power
Low cost
Integration
Plenary Talks, 13 March 2018, San Diego

## Slide 3
Th4A.2. Y. Ogiso et.al., “Ultra-High Bandwidth InP IQ Modulator
co-assembled with Driver IC for Beyond 100-GBd CDM”
Post deadline paper (OFC 2018) by NTT Lab
I ch.
Q ch.
Chart: 
EO response (dB)
Frequency (GHz)
Chart: 
High gain peaking design
OSNR: 29.2 dB
BER: 3.83×10-5
112 GBd
128 GBd
120 GBd
OSNR: 29.5 dB
BER: Error free
OSNR: 29.5 dB
BER: 6.68×10-3
□ Up to 128-GBd QPSK
□ 112-GBd 16QAM

## Slide 4
Bible of R&D
Top Leader in Communication
AT&T/ Bell Labs/Western Electric
Battle against FCC, Break-up in 1985
BSTJ ‘78 , LINAX Time Sharing Sys. !
1977, Tokyo
Reference on Bell Labs, Use to be
J. Morton (Bell Lab) “Organizing for Innovation” (1970)
W. Brooke Tunstall “Disconnecting Parties” (1985)
P. Temin, “The Fall of Bell System –A Study in Price and Politics- “ (1987)
J. Gertner, “The idea Factory –Bell Labs and Great Age of American Innovation” (2012)
L. Coldren ;
one of Legacies of Bell Lab.
S. E, Miller
Concept of PIC
Executive Meeting
NTT, WE & Bell Labs

## Slide 5: Number of LD Papers in Conference
1st ECOC (London, 1975）LD direct modulation (T. Ikegami)
3rd ECOC (Munich,1977) Fiber/Cable 30, LD 14
  Monomode fiber is promising (D. Marcuse) referring “connection loss, less than .2db by fusion splicing” (NTT, Feb.’76 Williamsburg)
8th ECOC (Cannes,1982) Fiber/Cable 39, LD 22, System 55
  WDM, Connector
  1.5μｍ Trans. with DFB-LD, Single-mode Fiber 104Km, @400Mb/s(NTT)
IOOC (Tokyo, ‘83) Fiber/Cable 61, LD 40, System 42
  OEIC(I. Hayashi); LiNbO₃, “not easy”
  Hard Screening (Ea, .7 eV-> .2 eV)
  Transmission Competition (Bit rate $ Distance)
OFC (San Diego, ‘96) LD(device only) 0 !
  Er doped Fiber Amp.(EDFA)
  VCL 1.54μｍ, 1Gb/s
“Just P-N Junction LD” was a Star in ‘70s and ‘80s

## Slide 6: History of LD
Direct Modulation of LD (my Doctor thesis , 1967)
  “Up to 400 MHz “ (1975, ECOC)
Room Temperature CW operation at short-wave length (Bell Lab, 1980)
Shift to long-wave length, since Fiber loss minimum
  Low connection loss by fusion (NTT,1977) , Mono-mode fiber could promising (ECOC ‘77)
Mode-partition noise (NTT,1975)
  Answer to “How degree single-mode oscillation under direct-modulation is necessary?”
  VICSEL could be answer, but Implementation ? Larry did !
Decided to use DFB LD (NTT,1982)
  Fabry-Perot to Grating-index
  “Ikegami became crazy, it’s just toy”
Competition of Transmission Capacity
Reliability; “Hard screening method”, leaved from Activation-energy theory (NTT,1985)
In ‘90’s

## Slide 7: History of LD
Direct Modulation of LD (my Doctor thesis , 1967)
  I said “Direct modulation possible up to 400 MHz “ (1975, #1 ECOC, London)
Room Temperature CW operation at short-wave length (Hayashi & Panish､Alferov1970)
Shift to long-wave length, since Fiber loss minimum
  Low connection loss by fusion (NTT,1977) , Mono-mode fiber could promising (ECOC ‘77)
Mode-partition noise (NTT,1975)
  Answer to “How degree single-mode oscillation under direct-modulation is necessary?”
  VICSEL could be answer, but Implementation ? Larry did !
Decided to use DFB LD (NTT,1982)
  Fabry-Perot to Grating-index
  “Ikegami became crazy, it’s just toy”
Competition of Transmission Capacity
Reliability; “Hard screening method”, leaved from Activation-energy theory (NTT,1985)
In ‘90’s

## Slide 8
T. Ikegami & Y. Suematsu,”Resonance-Like characteristics
of the Direct Modulation of a Junction Laser” Proc, IEEE 55,Jan. 1967
Resonance-Like phenomena
In Microwave Modulation
Bias Current
Modulation Frequency
Doctor Thesis
Bias Current
Intensity
Direct Modulation of Laser Diode (1967)

## Slide 9: LD Oscillation at Aug. 1971
Bell Labs tried “GaAsSb”
GaN not here
NTT Lab like “In“, Lucky !
“In” is a key material in Blue LD
(S. Nakamura, InGaN ‘94)
*Pumping Method
O: Optical
E: Electron
I: Injection
A:Avalanche
*
Oscillation Wavelength
Note; In 1962 N. Holonyack first succeeded in
Visible Red LD (‘62), GaAsP

## Slide 10: History of LD
Direct Modulation of LD (my Doctor thesis , 1967)
  I said “Direct modulation possible up to 400 MHz “ (1975, ECOC)
Room Temperature CW operation at short-wave length (Bell Lab; Hayashi & Panish､ Alferov, 1970)
Shift to long-wave length, since Fiber loss minimum
  Low connection loss by fusion (NTT,1976) , Mono-mode fiber could promising (ECOC ‘76)
Mode-partition noise (NTT,1975)
  Answer to “How degree single-mode oscillation under direct-modulation is necessary?”
  VICSEL could be answer, but Implementation ? Larry did !
Decided to use DFB LD (NTT,1982)
  Fabry-Perot to Grating-index
  “Ikegami became crazy, it’s just toy”
Competition of Transmission Capacity
Reliability; “Hard screening method”, leaved from Activation-energy theory (NTT,1985)
In ‘90’s

## Slide 11: History of LD
Direct Modulation of LD (my Doctor thesis , 1967)
  “Up to 400 MHz “(1975, ECOC)
Room Temperature CW operation at short-wave length(Bell Lab, 1970)
Shift to long-wave length, since Fiber loss minimum
  Low fiber connection loss by fusion (NTT,1976) , Mono-mode fiber could promising (Bell Lab, Marcateri ECOC ’76, Munich)
Mode-partition noise(NTT,1975)
  Answer to “How degree single-mode oscillation under direct-modulation is necessary?”
  VICSEL could be answer, but Implementation ? Larry did !
Decided to use DFB LD (NTT,1982)
  Fabry-Perot to Grating-index
  “Ikegami became crazy, it’s just toy”
Competition of Transmission Capacity
Reliability; “Hard screening method”, leaved from Activation-energy theory (NTT,1985)
In ‘90’s

## Slide 12
1.5um Transmission Experiment with DFB LD, 104km @ 400Mb/s, Normal SM Fiber (1982)
Post Deadline Paper @ ECOC’82, Cannes
Just experiment without Dispersion compensation of SM fiber but gave big Impact

## Slide 13: History of LD
Direct Modulation of LD (my Doctor thesis , 1967)
  “Up to 400 MHz “(1975, ECOC)
Room Temperature CW operation at short-wave length(Bell Lab, 1970)
Shift to long-wave length, since Fiber loss minimum
  Low connection loss by fusion (NTT, 1976) , Mono-mode fiber could promising (ECOC ’76, Munich)
Mode-partition noise (NTT,1975)
  Answer to “How degree single-mode oscillation under direct-modulation is necessary?”
  VCSEL could be answer, but Implementation ? Larry did !
Decided to use DFB LD (NTT,1982)
  Fabry-Perot to Grating-index
  “Ikegami became crazy, it’s just toy”
Competition of Transmission Capacity
Reliability; “Hard screening method”, leaved from Activation-energy theory (NTT,1985)
In ‘90’s

## Slide 14: Mode Partition Noise (1975)
Time resolved response measurement showed ;
Shape of Multi-mode spectrum was Random !
Random Noise (Cannot Compensate)
Noise Closes Eye-pattern in Digital Transmission
Decided to use DFB LD for coming over the Noise (‘82) in real (commercial) system “Ikegami became crazy, it is just a toy”
System people like 2 terminal rather than
3 terminal (Lobby discussion, IOOC’83)
Only Bell Lab. (K. Ogawa)
understand the Noise

## Slide 15
All Papers on InGaAsP LD from Japan were arranged in Poster Session! Why?
Answer to my Claim to Program Committee;
“For Fruitful Discussion (since Japanese presenter’s poor English)”
Move to Longwave Length (‘80)
Japan became leader in LD R&D

## Slide 16
CW Operation of 1500nm DFB Sept. 1981
Witness; J. C. Bouly (France Telecon)
Just Experiment in Lab !

## Slide 17: History of LD
Direct Modulation of LD (my Doctor thesis , 1967)
  “Up to 400 MHz “(1975, ECOC)
Room Temperature CW operation at short-wave length (Bell Lab, 1970)
Shift to long-wave length, since Fiber loss minimum
  Low connection loss by fusion (NTT,1976) , Mono-mode fiber could promising (ECOC ‘76)
Mode-partition noise(NTT,1975)
  Answer to “How degree single-mode oscillation under direct-modulation is necessary?”
  VICSEL could be answer, but Implementation ? Larry did !
Decided to use DFB LD(NTT,1982)
  Fabry-Perot to Grating-index
  “Ikegami became crazy, it’s just toy”
Competition of Transmission Capacity
Reliability; “Hard screening method”, leaved from Activation-energy theory(NTT,1985)
In ‘90’s
We enjoyed competition without Optical-amplifier (pumped by LD) / LDA which overcome penalty of functions

## Slide 18: History of LD
Direct Modulation of LD (my Doctor thesis , 1967)
  “Up to 400 MHz “(1975, ECOC)
Room Temperature CW operation at short-wave length (Bell Lab, 1970)
Shift to long-wave length, since Fiber loss minimum
  Low connection loss by fusion (NTT,1976) , Mono-mode fiber could promising (ECOC ‘76)
Mode-partition noise(NTT,1975)
  Answer to “How degree single-mode oscillation under direct-modulation is necessary?”
  VICSEL could be answer, but Implementation ? Larry did !
Decided to use DFB LD(NTT,1982)
  Fabry-Perot to Grating-index
  “Ikegami became crazy, it’s just toy”
Competition of Transmission Capacity
Reliability; “Hard screening method”, leaved from Activation-energy theory(NTT,1985)
In ‘90’s
We enjoyed competition without Optical-amplifier(pumped by LD) /LDA which overcome penalty of functions
INTERNET Society (1998~ )
Laser is widely used in our life, CD, etc.
PIC is common technology in Optical NWing and will be common technology in Robotics/AI era

## Slide 19
The First Generation in Bell Labs (Hayashi, Panish) were “PURGED”
The Second Generation (D. Dixon) succeeded in “stable” GaAlAs LD (1980)
“Do it Properly, you can get it” was answer to “How to make it ?” (#7 ISLC ’80)
The Third Generation (Gordon) had to collaborate with Hitachi to get InGaAsP for Reliability Test
NTT succeeded in Getting “Stable” InGaAsP LD by Screening Method(1983)
Reliability (1)
Very, very tough work for researches (Bell Lab & NTT Lab)
Hayashi’s Group succeeded in
Room Temperature CW Operation (‘70)

## Slide 20
Estimated Lifetime
Chaos
Report in NTT at 1981
10 k hrs.
InGaAs LD
Screening Method
(1983)
Reliability (2)
“Bell Lab’s Time”
GaAlAs LD
1 Mil. hrs.
Life Estimation
By “Activation Energy”
“NTT Lab’s Time”

## Slide 21
Screening Method (‘83)
Pre-selection of long life LD
by Non-destructive Stress Test
Common method
in industrial product
Note;
Traditional Lifetime-Estimation
Supposing Failure Distribution is Log-Normal
This method make sense in case of One Failure Mode
but reality is Many Failure Modes
(electrode, Facet, DH etc.)
Safety Condition
Dangerous !
Aging Current
Aging Temp.
Reliability (3)

## Slide 22: History of LD
Direct Modulation of LD (my Doctor thesis , 1967)
  “Up to 400 MHz “(1975, ECOC)
Room Temperature CW operation at short-wave length(Bell Lab, 1970)
Shift to long-wave length, since Fiber loss minimum
  Low connection loss by fusion (NTT,1976) , Mono-mode fiber could promising (ECOC ‘76)
Mode-partition noise(NTT,1975)
  Answer to “How degree single-mode oscillation under direct-modulation is necessary?”
  VICSEL could be answer, but Implementation ? Larry did !
Decided to use DFB LD(NTT,1982)
  Fabry-Perot to Grating-index
  “Ikegami became crazy, it’s just toy”
Competition of Transmission Capacity
Reliability; “Hard screening method”, leaved from Activation-Energy theory (NTT,1985)
In ‘90’s ; WDM, Fiber Amplifier pumped by LD, Chirping etc. (Bell Lab, Ting Lee etc.)
We enjoyed competition without Optical-amplifier(pumped by LD) / LDA which overcome penalty of functions
INTERNET Society (1998~ )
Laser is widely used in our life, CD, etc.
PIC is common technology in Optical NWing and will be common technology in Robotics/AI era

## Slide 23
Blue LD was Born by S. Nakamura
LEOS Annual Meeting, Nov. 1996, SFO
Big Discovery !
He enjoying UCSB life
“In” was key (patent, NTT, 1988)
InGaN LD
Nobel Prize in Physics (Eminent Engineer !)
20 hrs
Drive Current
keeping Constant Power-output

## Slide 24: History of LD
Direct Modulation of LD (my Doctor thesis , 1967)
  “Up to 400 MHz “(1975, ECOC)
Room Temperature CW operation at short-wave length(Bell Lab, 1970)
Shift to long-wave length, since Fiber loss minimum
  Low connection loss by fusion (NTT,1976) , Mono-mode fiber could promising (ECOC ‘76)
Mode-partition noise(NTT,1975)
  Answer to “How degree single-mode oscillation under direct-modulation is necessary?”
  VICSEL could be answer, but Implementation ? Larry did !
Decided to use DFB LD(NTT,1982)
  Fabry-Perot to Grating-index
  “Ikegami became crazy, it’s just toy”
Competition of Transmission Capacity
Reliability; “Hard screening method”, leaved from Activation-energy theory(NTT,1985)
WDM (Bell Lab)
We enjoyed competition without Optical-amplifier(pumped by LD) / LDA which overcome penalty of functions (~ 1995) !!
INTERNET Society (1998~ )
Laser is widely used in our life, CD, Projection Mapping etc.
PIC is common technology in optical NWing and will be common technology in Robotics/AI era

## Slide 25
Once Upon a Time,,

## Slide 26
Don Scifres; good business with
High-power LD not Communication LD
Morton Panish
Room Temperature CW operation ‘70 with Hayashi
but not be appreciated
Received KYOTO Award (’01)

## Slide 27
Ibuka, Sony
IEEE Fellow授与式(1986)
’80’s Int. Standardization Activity, Convener of IEC/TC48 EU Project ECOC
’86 IEEE Fellow, joined Professional Society, America
IEEE/LEOS
Japan was very, very far from East/West World
up to ’90s
Attended ECOC, London (1975)
IEC Meeting
My International Activities
Chair EU-DG13
Ibuka Prize
for consumer electronics
Appliance (1986)
Convener IEC/TC48

## Slide 28: From LD to “Mission to Mars”
Visit Kennedy Space Center
Lunching “Galileo” (OFC 89)
Chair
Japanese Space Activities Commission (’07)
After Last Lunching of Space Shuttle 136, Visited Elon Musk (11 July, ‘11)
JAXA
Space X / Tesla

## Slide 29
Optics & Photonics News (1995)
“80 Years of Optics”
What will happen, Tomorrow ?

## Slide 30
Congratulation, Larry !
Per aspera ad astra !
PIC
VCSEL
(Under Aging, Enjoy Happy Life !)